## Slide 1
DUAL MODE VISION-GUIDED ROBOTIC ARM
A Project report submitted in partial fulfilment of the requirement for the degree of the
BACHELOR OF TECHNOLOGY
IN
ELECTRONICS AND COMMUNICATION ENGINEERING
SUBMITTED BY
CHADARAM MAANAS
Reg No: 321106512004
BORA ABHINAV
Reg No: 321106512005
CHEPURI NATRAJ
Reg No: 321106512006
MANNAVA SREE PARDHEEV KUMAR
Reg No: 321106512028
UNDER THE ESTEEMED GUIDANCE OF
Prof. P. RAJESH KUMAR M.E., Ph.D.
Professor
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
ANDHRA UNIVERSITY COLLEGE OF ENGINEERING
VISAKHAPATNAM – 530003
2022–2026

## Slide 2
Abstract
Abstract | 2/10
🎯 OBJECTIVE
This project develops a 6-DOF robotic arm capable of autonomous object sorting via computer vision and human-in-the-loop gesture control, switching seamlessly between modes without physical intervention.
🏗️ ARCHITECTURE
Hardware: 6× MG996R servos on a metal arm kit, ESP8266 microcontroller, MPU6050 IMU. Software: ROS2 Jazzy, Gazebo Harmonic for physics simulation, RViz for visualisation, YOLOv8 for hand/object detection.
📊 PROGRESS
Milestones complete: (1) hardware procured; (2) custom URDF developed after iterative adaptation; (3) arm simulated in Gazebo & RViz; (4) initial ESP8266 servo control written; (5) YOLO hand detection tested — pipeline integration ongoing.
🔬 SIGNIFICANCE
Dual-track development (hardware + software simulation) validates each track independently, reducing integration risk and ensuring a testable prototype at every phase of the project lifecycle.

## Slide 3
System Architecture & Tools
Two parallel development tracks converging into one unified system
System Architecture & Tools | 3/10
Hardware Track
• 6-DOF Metal Servo Arm Kit
• 6× MG996R Servo Motors
• ESP8266 Microcontroller
• IMU Sensor (MPU6050)
• 5V / 10A Dedicated PSU
Software Track
• ROS2 Jazzy Jalisco
• Gazebo Harmonic (Simulation)
• RViz (Visualisation)
• YOLOv8 (Hand Detection)
• OpenCV + MediaPipe
IMU / Camera Feed → ESP8266 / ROS2 → Servo Motor Commands → Arm Motion

## Slide 4
Phase 1 — Hardware Procurement
Phase 1 — Hardware Procurement | 4/10
✅ Completed
OVERVIEW
All primary hardware components were ordered and received. Component selection was finalised based on torque, availability, and ESP8266 compatibility.
OUTCOME
All hardware is on hand and ready for wiring and firmware integration.
01
Component Selection
Six MG996R servos (9–11 kg·cm), ESP8266 NodeMCU for Wi-Fi PWM control, MPU6050 IMU for 6-axis feedback. Initial plan called for 4 servos; upgraded to 6 for full DOF.
02
Procurement & Delivery
Components sourced and ordered. Arm kit, servos, ESP8266, IMU, and 5V/10A PSU all received and inspected.
03
Inventory Verified
6× MG996R, 1× ESP8266 NodeMCU, 1× MPU6050, 1× 6-DOF frame + claw gripper, 1× 5V/10A PSU — confirmed complete.

## Slide 5
Phase 2 — 3D Model & URDF Development
Phase 2 — 3D Model & URDF Development | 5/10
✅ Completed (Multiple Iterations)
OVERVIEW
A URDF is mandatory for Gazebo simulation. No pre-existing URDF matched our hardware, so one was created from an adapted open-source reference.
OUTCOME
Working Xacro URDF produced and integrated into the ROS2 workspace package my_arm_description.
01
Challenge: No Matching URDF
The purchased 6-DOF metal arm kit has no freely available 3D model or URDF online. Without a URDF, simulation and motion planning are impossible.
02
Reference Model Located
ferasboulala/five-dof-robot-arm on GitHub was used as a base. Mesh proportions and joint placements were studied against the physical hardware.
03
Iterative Adaptation
Multiple attempts: adjusting link lengths, correcting joint axes, converting to ROS2 Xacro format, adding the 6th joint and gripper, fixing mesh collision/inertia errors.
04
Working Model Achieved
Stable Xacro URDF produced with 6 correctly defined joints, link inertias, and collision geometry — sufficient for simulation and motion planning.

## Slide 6
Phase 3 — Simulation in Gazebo & RViz
Phase 3 — Simulation in Gazebo & RViz | 6/10
✅ Completed
OVERVIEW
With the URDF ready, the arm was loaded into Gazebo Harmonic (physics sim) and RViz (kinematic visualisation) as the primary testbed before hardware deployment.
OUTCOME
Arm simulates correctly in Gazebo with physics-accurate joint motion. Trajectory commands execute reliably via ROS2 topics.
01
RViz Visualisation
Loaded via display.launch.py. joint_state_publisher_gui sliders confirmed all 6 joints move correctly. Link transforms verified.
02
Gazebo Harmonic Launch
Arm spawned via gazebo.launch.py. gz-ros2-bridge configured to relay joint states. JointTrajectoryController from ros2_control activated.
03
Controller Verification
ros2 control list_controllers confirmed joint_trajectory_controller and joint_state_broadcaster active.
04
Motion Testing
Test trajectory commands published via ros2 topic pub. Pick-place sequences and joint-level position commands prototyped in simulation.

## Slide 7
Phase 4 — Servo Motor Control (ESP8266)
Phase 4 — Servo Motor Control (ESP8266) | 7/10
🔄 In Progress
OVERVIEW
Initial development of servo motor control firmware on the ESP8266 began in parallel with simulation. This is the hardware counterpart to the simulated JointTrajectoryController.
OUTCOME
Individual servo control functional. Multi-servo coordination and ROS2–ESP8266 bridge are the next steps.
01
ESP8266 PWM Control
ESP8266 NodeMCU selected for built-in Wi-Fi and PWM output. Will receive joint angle commands and translate them to PWM signals for all 6 MG996R servos.
02
Signal Generation
MG996R servos need 50 Hz PWM, 500–2500 µs pulse width for full motion range. Initial firmware maps angle → pulse width and generates signals on digital IO pins.
03
Initial Tests
Preliminary tests on individual servo motors complete. Smooth angle transitions with configurable speed implemented to prevent jerky motion.

## Slide 8
Phase 5 — Computer Vision Integration (YOLO)
Phase 5 — Computer Vision Integration (YOLO) | 8/10
🔄 Under Development
OVERVIEW
A YOLOv8-based pipeline was developed to detect a human hand and convert that detection into servo movement commands. This is the core intelligence of gesture control mode.
OUTCOME
Hand detection functional in isolation. Full pipeline integration into ROS2 + servo chain is the current blocker under active debugging.
01
YOLOv8 Model Setup
YOLOv8 (Ultralytics) configured on NVIDIA RTX 3060 with CUDA 12.1 for accelerated inference. Targeting real-time >30 FPS performance.
02
Detection → Command Pipeline
Intended: camera → YOLOv8 bounding box → centroid → IK → 6 joint angles → ESP8266 servo commands. Partially implemented.
03
Integration Issues Found
Latency spikes in detection-to-command loop, coordinate mapping calibration errors, and serialization issues passing YOLO output into ROS2 topics.
04
Current Status
YOLO detects hands reliably in isolation. End-to-end integration from detection to servo command under active debugging and expected to resolve in next cycle.

## Slide 9
Challenges & Current Status
Dual-track development: each track validated independently, converging at integration
Challenges & Current Status | 9/10
Hardware Track
COMPLETED
✅ All components procured
✅ Specs verified
✅ ESP8266 PWM firmware written
✅ Individual servo response tested
PENDING
⏳ Full arm assembly & wiring
⏳ Multi-servo coordinated control
⏳ ROS2 ↔ ESP8266 serial bridge
⏳ IMU integration
Software Track
COMPLETED
✅ URDF created after iterative adaptation
✅ Arm visualised in RViz
✅ Gazebo simulation running
✅ ros2_control JTC active
✅ YOLOv8 detection working in isolation
PENDING
⏳ YOLO → ROS2 command pipeline
⏳ Camera-to-workspace calibration
⏳ MoveIt2 motion planning
⏳ Autonomous mode logic
Key Challenge: The most significant obstacle was the absence of a ready-made URDF for the purchased arm kit, requiring multiple iterative reconstruction attempts before a working simulation model was produced.

## Slide 10
Next Steps & Roadmap
Structured development path — testable artefact at every phase
Next Steps & Roadmap | 10/10
P1
Hardware Assembly
→ Wire all 6 servos
→ Connect IMU
→ PSU integration
→ Bench test all joints
P2
ROS2 ↔ Hardware Bridge
→ ESP8266 serial bridge node
→ ROS2 JointTrajectory → servo
→ Real HW controller test
→ ros2_control HW interface
P3
Vision Pipeline Fix
→ Debug YOLO → ROS2 pipeline
→ Camera calibration
→ Coordinate mapping
→ Latency test
P4
Full System Integration
→ Autonomous sorting mode
→ Gesture control (local)
→ Mode switching logic
→ 50-cycle stress test
Each phase produces a standalone demonstrable prototype — ensuring progress is always presentable regardless of final timeline.